## Slide 1: Software Status Report
R.J.Barnes

## Slide 2
Digital Receiver Drivers:
  gc214if GC214 card at IF frequency
  gc214hf GC214 card at HF frequency
  gc214TSif GC214/TS card at IF frequency
  gc214TShf GC214/TS card at HF frequency
(Lots of thanks to Todd and Dieter)
Drivers appear identical to the rest of the software so no customization for different radars
Radar Operating System

## Slide 3
Status of Stereo:
  Stereo converted to the new version of ROS
  Implemented for analogue receiver
  Implemented for digital receivers
  Digital receiver driver adapted to allow multiple cards
  The Stereo software has been installed and tested using digital receivers at Blackstone.
Radar Operating System

## Slide 4
Implementation of “tauscan”
  Ray and Kjellmar’s new pulse sequence and lag table
    Lag table has multiple pulse pairs for a single lag
    Best pair are used for analysis
  New analysis libraries and tools to support it
Still to do:
  Implement a stereo version
  Add a variables to the RawACF file to indicate we are using a “tauscan mode”
    Currently store only the first set of lag pairs
    Need to store the full lag table
  Modify make_fit to autodetect “tauscan” RawACF files and process them automatically
Radar Operating System

## Slide 5
Storage of I&Q samples
  Capability was developed to diagnose digital receiver card
  Developed xscope as a virtual oscilloscope
  Developed rawdump to look at actual sample numbers
  Both diagnostic tools
    run from the command line
    produced a single monolithic file
    did not contain all the radar operating parameters
Radar Operating System

## Slide 6
Storage of I&Q samples - iqwrite
  Similar to rawacfwrite and fitacfwrite
  Stores files every 2 hours in DataMap format.
  File contains the Radar Parameter Block and I&Q samples.
  Samples are accumulated in a shared memory buffer maintained by the Control Program
  iqwrite can be turned on and off in the control program
Files are big!
Radar Operating System

## Slide 7
Currently at version 2.12
  Numerous bug fixes
  Added tools for working with I&Q data:
  make_raw make a RawACF file from I&Q data
  make_rawex make a RawACF file from I&Q data (tauscan)
  make_iqinx make an index file to an IQdat file
  trim_iq trim a section from an IQdat file
  iq_plot simple xterminal display of I&Q data
Analysis Software

## Slide 8
The IDL libraries include routines for reading and writing I&Q samples from an Iqdat file.
Example code is included
An IDL implementation of the full ACF algorithm would be an excellent educational tool
  Good project for a student
Analysis Software

## Slide 9
Added support for multi-page documents
Previously tools could only produce a single plot
  difficult to review lots of data
New tools provided for working with multi-page documents
    rplotcat concatenate multiple rplot files into one multi-page file
    rplotgrid reformat a multi-page rplot file into a multi-panel plot
    rplotindex generate an index to a multi page rplot
    rplotmultiplex construct a multi-page rplot file from multiple sources
    rplotpages count the number of pages in a multi-page rplot document
    rplottrim extract pages from a multi-page rplot document
RST Graphics

## Slide 10
Generating a multi-panel plot:
rplotcat ????.rp.xml > multipage.rp.xml
rplotgrid -width 640 -height 960 \
-numx 2 -numy 3 \
multipage.rp.xml > output.rp.xml
RST Graphics

## Slide 11
New compositing tools
Allows plots to be constructed from layers of data (like GIS)
Multiple data sources (not just SuperDARN) can be composited together
Full Alpha Channel blending (translucency)
No other scientific visualization software can do this
RST Graphics

## Slide 12
RST Graphics

## Slide 13
Scalable Vector Graphics (SVG) output
The existing rplot output is SuperDARN specific
SVG is a W3 standard
Supported by many graphics editors
Supported by many browsers
RST Graphics

## Slide 15
One more thing……